## Slide 1: F1/10 Research Summary
Peter Guarner

## Slide 2: Papers Reviewed
A Planning and Control System for Self-Driving Racing Vehicles
  Optimization of vehicle lap time with autonomous race car
Localization-based software architecture for 1:10 scale autonomous car
  Implementation of F1/10 project

## Slide 3: Hardware
LiDAR sensor
  Range measurements with high frequency emission of laser pulses.
  Generates dense ‘point clouds’ of gathered measurements
IMU sensor
  Accelerometer and gyroscope to determine acceleration, speed, and orientation
  Prone to vibration errors and bias drift error
Wheel Tachometer
  Provides additional speed measurement and travel displacement
ROS Computer
Microcontroller with Bluetooth
Source: Reference 2))

## Slide 4: Mapping and Localization
Mapping
  Using range measurements and odometry to predetermine environment: boundaries and expected path.
  Helps plan the desired path for the vehicle to follow
  Processed on separate ROS nodes since computations are intensive
  Three ROS mapping schemes:
          Hector Mapping
          Gmapping
          Cartographer
Localization
  Use relative sensor measurements to estimate vehicle state
  Fusing sensor data helps determine better state estimate
  Monte Carlo algorithms uses point probabilities to help refine state estimate
  Normally acquired by integrating acceleration and speed measurements
  Aided with PID controller for actuators
Source: Reference 1))

## Slide 5: Optimization process
Mapping: conduct calibration lap to determine environment boundaries.
Determine optimal steering around track based on traction limits for a constant speed. Save trajectory as a reference.
Optimize speed input incremental points on the path.
Drive the track while keeping as close to the reference as possible.
  Localization: estimate state at each point and compare to desired
  Feedback errors from comparison to desired path and PID controller
  Fuse measurements together for better estimation: Kalman filter/particle filter.
  Determine localization errors for post-race tuning or reconfiguration
Source: Reference 1))

## Slide 6: References
Caporale, D., Fagiolini, A., Pallottino, L., Settimi, A., Biondo, A., Amerotti, F., … Venturini, L. (2018). A Planning and Control System for Self-Driving Racing Vehicles. 2018 IEEE 4th International Forum on Research and Technology for Society and Industry (RTSI). doi: 10.1109/rtsi.2018.8548444.
Gotlib, A., Lukojc, K., & Szczygielski, M. (2019). Localization-based software architecture for 1:10 scale autonomous car. 2019 International Interdisciplinary PhD Workshop (IIPhDW). doi: 10.1109/iiphdw.2019.8755418.